## Slide 1
Crispy: a Python-based user interface for core-level spectroscopy calculations
Marius Retegan
Algorithms & scientific Data Analysis (ADA) Group
European Synchrotron Radiation Facility (ESRF)

## Slide 2: Semi-empirical multiplets: the early days
B.T. Thole et al.,
Phys. Rev. B, 1985
F.M.F. de Groot et al.,
Phys. Rev. B, 1990

## Slide 3: Quanty: a modern approach to multiplets calculations
Quanty is a powerful and versatile library, but…
You will have to write code to perform calculations.
The program is very forgiving and can take time to spot an error.

## Slide 4: Crispy: graphical user interface for multiplet calculations
Calculations:
  transition metals, lanthanides, and actinides
  XAS, XMCD, X(M)LD, XPS, and RIXS
  many edges
  Oh, D4h, C3v, Td, and D3h symmetries
Additional features:
  logging console to display the progress
  dialog showing the details of a calculation
  interactive broadening
  easy-to-use installers for Windows and macOS
  Jupyter notebook interface

## Slide 5: Getting the software
http://esrf.eu/computing/scientific/crispy
crispy + esrf

## Slide 6: Things to remember!
Any modification to the combo boxes will reset all parameters to default values.
Always press Return (Enter) after changing a value in any of the input boxes.

## Slide 7: Calculating the L2,3–edge XAS spectrum of titanium(IV)

## Slide 8: Theory and calculations
de Groot et al., J. Chem. Minerals, 1992

## Slide 9: Atomic multiplets
Calculate the XAS spectrum at the L2,3 edges of Ti4+ in spherical symmetry. Set the Lorentzian broadening to 0.1 and the Gaussian broadening to 0.0. Leave all the other parameters to their default values. How many transitions are visible in the spectrum?
Run a calculation with the scaling of the 2p spin-orbit coupling constant, ζ(2p), set to 0.5. After the calculation finishes, set this value back to 1.0 and run a second calculation with the 3d spin-orbit coupling ζ(3d) set to 0.5. Which interaction affects the most the energy separation between the L2 and L3 edges? Check that the energy separation between the two edges is close to 3/2·ζ(2p).
Perform three calculations using 0.8, 0.4, and 0.0 for scaling the Slater integrals, Fk and Gk. What is the influence of electronic repulsions on the spectrum?

## Slide 10: Crystal-field multiplets
Set the scaling factors for the Slater integrals back to 0.8. Re-enable the crystal field and change the 10Dq value to 2.0 eV.
Change the Lorentzian broadening to 0.2, 0.4, 460. This will apply a 0.2 eV broadening at the L3 edge and a 0.4 eV at the L2 edge and will change between the two broadenings at 460 eV.
Run a set of calculations with 10Dq ranging from 0 to 2.0 eV in steps of 0.5 eV. Plot the resulting spectra. What is the influence of the crystal field splitting?
Set the 10Dq value to 2.0 eV and switch off the Slater integrals and the 3d spin-orbit coupling. How many transitions does the calculated spectrum have?

## Slide 11: Following spin transitions in iron compounds

## Slide 12: Using K pre-edge XAS to identify spin states
Write down the electronic configuration of Fe3+. Show that there are two ways to fill the 3d orbitals, leading to a high spin (S = 5/2) and a low spin ground state (S = 1/2).
Run two K pre-edge calculations for Fe3+ in an octahedral crystal field, one with 10Dq set to 2.0 eV and 3.3 eV.
Change the 10Dq value from 2.6 to 3.6 eV in steps of 0.2 eV. At what value do you observe the spin transition?
Westre et al., J. Am. Chem. Soc., 1997

## Slide 13: Application of the XMCD sum-rules

## Slide 14: XMCD Sum rules for L2,3 edges
Jafri et al., Inorg. Chem., 2016

## Slide 15: The magneto-optical sum rules

## Slide 16: Sum rules in practice
The sum rules can provide very useful information on the magnetic electronic
structure by separating the orbit and spin parts of the magnetization.
Origin of problems in the application of the sum rules:
  Removal of the transitions towards continuum states is done by subtracting parameterized arctangent functions.
  The cutoff energy between L3 and L2 edges in the XMCD spectrum.
  Intermixing of L3 and L2.

## Slide 17: Experimental data
Experimental details:
  the metal atom in FeTp is Fe3+
  temperature (T = 2 K)
  magnetic field (B = 6.5 T)
Measured spectra: http://bit.ly/multiplets

## Slide 18: Calculations using octahedral (Oh) symmetry
 | ⟨Sz⟩ | ⟨Lz⟩ | ⟨Tz⟩
Jafri et al. | −0.1786 | −0.8521 | −0.0523
Calculate the spectrum using the following parameters:
    Lorentzian FWHM: 0.5
    Gaussian FWHM: 0.24
    scale factors: Fk = Gk = 0.7, zeta = 1.0
After the first calculation, open the “Details” dialog and normalize the spectrum to the maximum.
Increase the 10Dq value in steps of 0.5. Note the effect on the calculated spectrum. Are any features that start appearing in the spectrum for larger 10Dq? Follow the changes in the expectation value of the ⟨Sz⟩ operator.
Note the expectation values of the spin (S), orbital (L), and magnetic dipole (T) operators for 10Dq = 2.8 eV. How do they compare with the calculations from the original publication?

## Slide 19: Ligand field calculation in octahedral symmetry
 | ⟨Sz⟩ | ⟨Lz⟩ | ⟨Tz⟩
Jafri et al. | −0.1704 | −0.7754 | −0.0594
Hocking et al., J. Am. Chem. Soc., 2006
Note the additional features appearing in the spectrum and the changes in the expectation values; compare them with the ones from the original publication.
Add the metal-ligand hybridization charge transfer (MLCT) term with the following parameters:
Δi = 3.0, Δf = 3.4, V(eg) = −0.8, V(t2g) = 1.8.

## Slide 20: In search of the missing peak
Change the symmetry to C3v and rerun the calculation using the following parameters for the crystal field:
  Dq = 0.28 eV (≡ 10Dq = 2.8 eV)
  Dσ = 0.07 eV
  Dτ = 0.12 eV
Did you manage to reproduce the feature f?
t2g
eg
e
a1
e

## Slide 21: Utility of multiplets calculations
What is the value of ⟨Tz⟩?
Test the validity of the sum rules and determine the origin of their potential failures.

## Slide 22: Crystal field and covalency effects in uranates

## Slide 23: Crystal field and covalency effects in uranates

## Slide 24: Crystal field and covalency effects in uranates
1) Calculate the atomic M4 spectrum for U5+ using the following parameters:
  scale factors: Fk = Gk = 0.7
  Lorentzian FWHM: 0.35 eV
  Gaussian FWHM: 0.8 eV
2) Add a crystal field contribution with Wybourne’s parameters:
  B40 = 2.03 eV
  B60 = 0.17 eV
3) Finally, add the hybridization term with the ligands (LMCT):
  Δ = 4.0 eV,
  U(5f,5f) = 3.5 eV
  U(3d,5f) = 6.0 eV
  Vi = 1.2 eV, and Vf = 0.9 eV